Reading Potentiometer
- Also known as voltage divider
- When powered with 5v , the middle pin outputs a voltage between 0 to 5 depending on the position of the knob

---
Circuit

---
analogRead()
- Reads the value from the specified analog pin
- it will map input voltages between 0 and 5 volts into integer values between 0 and 1023 - 10 bit ADC
- Resolution
  5/1024 = 4.9mv

---
Change the speed of led

---
LED On/Off By Position

---
Volume Controller
100 Ohm R

---
Volume Knob

---
Sense your Environment
Photoresistor
- Changes resistance based on how much light the sensor receives
- Voltage Divider is used with sensor

---
LDR R - 10k

---
On/Off Led

---
How Bright is Out there

---
Servo Control
- Servo motors can turn into a specified position – usually 1800
- Varying pulse width of output voltage will move servo to specific position
- Servo Library is used to control Servo

---
Library
- Libarary is a group of Funtions
- Libraries are used to extend the functionality of skecthes
- Servo is one of the preinstalled library

---
- #include is a preprocessor command, inserts a library into sketch
- servo library adds new commands that let you control servo

---
To Control Servo
- Create a “Servo object”
- Attach it to Digital Pin
- Write number of degrees to move – 0 to 180

---
Sweep It

---
Control the Servo Position