What is Arduino ?
The Arduino is a tiny computer system that can be programmed with your instructions to interact with various forms of input and output

---
Quick Tour	of Arduino
USB Connector
- Connects Arduino to Computer
- To Supply Power
- Upload Instructions to Arduino
- Send and Receive Data

---
Quick Tour	of Arduino
- Power the Arduino with DC 9-12V plug

---
Quick Tour Arduino
MicroController
- Brain of the Arduino
- Executes Instructions
- Contains Memory

---
Quick Tour Arduino
Analog Inputs
- Six Analog In Pins
- Measure Electrical Signals vary in voltage

---
Quick Tour of Arduino
- Power Connections
- External RESET

---
Quick Tour of Arduino
Digital Input and Output Pins
- Detect the prescence of signal or Can Generate on Command
- ‘ ~ ‘ Labelled pins can generate varying electrical signal

---
Quick Tour of Arduino
On Board Led’s
- TX, RX light up when Data being Transmitted and Received
- L is connected to Digital Pin 13

---
Software - Download
Arduino.cc/en/Main/Software
Select Installer

---
Installation
- Double click on the Downloaded Exe File
- Allow OS to install Drivers

---
installation

---
Installation - Driver
- Connect Arduino to Computer using USB Cable
- Open Device Manger
- Look under Ports
- Note Arduino UNO COM port

---
IDE – Test Run
- Double Click on the Arduino Icon in Desktop
- The Tab is known as Sketch
- It Contains the program that tells your board what to do

---
 Test Run - Blink It
Go to File->Examples-> Basics-> Blink and click on it

---
 Test Run - Blink It
- Select Board type in Tools -> Board
- Select UNO
- Select COM port noted Previously in Tools -> Port

---
Test Run - Upload
- Click the upload button
- you should see the RX and TX leds on the board flashing
- After few seconds on board led blinks