Reading Potentiometer
- Also known as voltage divider
- When powered with 5v , the middle pin outputs a voltage between 0 to 5 depending on the position of the knob

---
Circuit

---
analogRead()
- Reads the value from the specified analog pin
- it will map input voltages between 0 and 5 volts into integer values between 0 and 1023 - 10 bit ADC
- Resolution
  5/1024 = 4.9mv

---
Volume Controller