Reading Potentiometer
- Also known as voltage divider
- When powered with 5v , the middle pin outputs a voltage between 0 to 5 depending on the position of the knob

---
Circuit

---
analogRead()
- Reads the value from the specified analog pin
- it will map input voltages between 0 and 5 volts into integer values between 0 and 1023 - 10 bit ADC
- Resolution
  5/1024 = 4.9mv

---
Change the speed of led

---
LED On/Off By Position

---
Volume Controller
100 Ohm R

---
Volume Knob

---
Sense your Environment
Photoresistor
- Changes resistance based on how much light the sensor receives
- Voltage Divider is used with sensor

---
LDR R - 10k

---
On/Off Led

---
How Bright is Out there

---
Servo Control
- Servo motors can turn into a specified position – usually 1800
- Varying pulse width of output voltage will move servo to specific position
- Servo Library is used to control Servo

---
Library
- Libarary is a group of Funtions
- Libraries are used to extend the functionality of skecthes
- Servo is one of the preinstalled library

---
- #include is a preprocessor command, inserts a library into sketch
- servo library adds new commands that let you control servo

---
To Control Servo
- Create a “Servo object”
- Attach it to Digital Pin
- Write number of degrees to move – 0 to 180

---
Sweep It

---
Control the Servo Position

---
Serial Communication
- So far we only used led’s to display the output
- sketch can use usb connection to send messages to or receive them from your computer

---
Serial Monitor

---
Hello world from Arduino
- Upload it
- Open Serial monitor

---
Starting the Serial Monitor
  - Before we can use the Serial Monitor, we need to activate it by adding this function to our sketch in void setup() :
    Serial.begin(9600);
  - 9600 is the speed at which the data will travel between the computer and the Arduino known as Baud Rate
  - This value must match the speed setting at the bottom right of the Serial Monitor

---
- To send text to the Serial Monitor to be displayed in the output window,you can use Serial.print
- You can also use Serial.println to display text and then force any following text to start on the next line

---
Sense your Environment
- This project uses DHT11 sensor
- Used to sense Temparature and Humidity
- Dht library is used for interfacing

---
Adding External Libraries
- Go to Sketch -> Include Library and click on the Mange libraries
- You will get libarary manager

---
- In search Enter dht11
- Select DHT sensor Library
- And click install

---
Serial Input