What is Arduino ?
The Arduino is a tiny computer system that can be programmed with your instructions to interact with various forms of input and output

---
Quick Tour	of Arduino
USB Connector
- Connects Arduino to Computer
- To Supply Power
- Upload Instructions to Arduino
- Send and Receive Data

---
Quick Tour	of Arduino
- Power the Arduino with DC 9-12V plug

---
Quick Tour Arduino
MicroController
- Brain of the Arduino
- Executes Instructions
- Contains Memory

---
Quick Tour Arduino
Analog Inputs
- Six Analog In Pins
- Measure Electrical Signals vary in voltage

---
Quick Tour of Arduino
- Power Connections
- External RESET

---
Quick Tour of Arduino
Digital Input and Output Pins
- Detect the prescence of signal or Can Generate on Command
- ‘ ~ ‘ Labelled pins can generate varying electrical signal

---
Quick Tour of Arduino
On Board Led’s
- TX, RX light up when Data being Transmitted and Received
- L is connected to Digital Pin 13

---
Software Installation - Download
Arduino.cc/en/Main/Software